## Slide 1
Sarah Berendes
Session 3
RLI, 17.09.2019
© Reiner Lemoine Institut
Oemof Workshop Week Component Models
oemof v0.3.1

## Slide 2: Agenda
Basic Components
Discussion
Introduction
Components
Custom Components
Current Development

## Slide 3: Intro: Components (Models)
We define all technologies (e.g. power plants), energy carriers (e.g. diesel) and demands (e.g. electricity demand) of the physical energy system as components. A component model describes an abstract representation of a component in the physical system.

## Slide 4: Intro: oemof Characteristics
Modularity and generalization have been key principles behind oemof

## Slide 5: Intro: oemof Package Structure

## Slide 6: Package Structure: oemof.solph
Relevant modules that contain components:
network (basic components)
components
custom
Generic
For developers
Reduced to a common model concept
specific
For users
Concrete for a specific use case
basic
custom
components

## Slide 7: Reminder: oemof Modelling Principles
(Mixed Integer) Linear Programming + Graph Theory
Models composed of Nodes and Edges
  Node / Bus or Component (oemof)
  Edge / Flow
2 Components can’t be directly connected, Bus required in between
Bus balance (example)
Parameterization mainly done within Flows

## Slide 8: Overview Basic Components
Class: oemof.solph.network
API-Documentation: https://oemof.readthedocs.io/en/stable/api/oemof.solph.html#module-oemof.solph.network
Note! See example and further information here:
https://github.com/smartie2076/oemof_workshop/tree/master/Day_2_Components_Oemof/3_3_oemof_component_models_oemof_solph.ipynb
Sink
Source
Transfomer

## Slide 9: Overview Components
GenericStorage
GenericCHP
ExtractionTurbineCHP
OffSetTransformer
Class: oemof.solph.components
API-Documentation: https://oemof.readthedocs.io/en/stable/api/oemof.solph.html#module-oemof.solph.components

## Slide 10: Components.GenericStorage
Description | Model class to model basic characteristics of (energy) storages
Input(s)/Output(s) | n/m
Bases | Transformer
Balance | Linear
Parameterization (not complete) | nominal_storage_capacity, initial_storage_level, balanced, loss_rate, inflow_conversion_factor, outflow_conversion_factor, min_storage_level, max_storage_level
Examples | Battery Energy System, Pumped Hydro Storage, etc

## Slide 11: Components.GenericCHP
Description | Component GenericCHP to model combined heat and power plants.
Input(s)/Output(s) | n/m
Bases | Transformer
Balance | Mixed Integer Linear
Parameterization (not complete) | fuel_input, électrical_output, heat_output, beta (power loss index) back_pressure
Examples | Combined Cycle, Back pressure turbines

## Slide 12: Components.ExtractionTurbineCHP
Description | Model combined heat and power plant with extraction turbine
Input(s)/Output(s) | n/m
Bases | Transformer
Balance | Linear
Parameterization (not complete) | conversion_factor, conversion_factor_full_condensation (no tapped flow extraction)
Examples | Simplified CHP model, Extraction Turbine

## Slide 13: Components.OffsetTransformer
Description | Model tansformers with an offset
Input(s)/Output(s) | n/m
Bases | Transformer
Balance | Mixed Integer Linear
Parameterization (not complete) | conversion_factor, conversion_factor_full_condensation (no tapped flow extraction)
Examples | Diesel Generator,

## Slide 14: Components.OffsetTransformer
Description | Model tansformers with an offset
Input(s)/Output(s) | n/m
Bases | Transformer
Balance | Mixed Integer Linear
Parameterization (not complete) | coefficients (y-intersection and slope)
Examples | Diesel Generator, CAES

## Slide 15: Overview Customs
Link
ElectricalLine
GenericCAES
Class: oemof.solph.custom
API-Documentation: https://oemof.readthedocs.io/en/stable/api/oemof.solph.html#module-oemof.solph.customs

## Slide 16: Custom.Link
Description | To directly link two nodes Buses
Input(s)/Output(s) | n/m
Bases | Pyomo
Balance | Linear
Parameterization (not complete) | conversion_factors
Examples | Transshipment_link
Note!
Experimental
Needs improvment

## Slide 17: Custom.ElectricalLine
Description | To do linear optimal power flow calculations based on angle formulation.
Input(s)/Output(s) | either in or out
Bases | Flow
Balance | Mixed Integer Linear
Parameterization (not complete) | reactance
Examples | Grid model
Note!
connected buses need to be of the type ElectricalBus.
It does not work together with flows that have set the attr.`nonconvex`
Input and output of this component are set equal, therefore just use either only the input or the output to parameterize.
Default attribute min of in/outflows is overwritten by -1 if not set differently by the user

## Slide 18: Custom.ElectricalBus
Description | Bus object to be used with Electrical Line for LOPF
Input(s)/Output(s) | n/m
Bases | Bus
Balance | Mixed Integer Linear
Parameterization (not complete) | slack max_voltage_angle min_voltage_angle
Examples | Grid model

## Slide 19: Custom.GenericCAES
Description | To model a arvitrary compressed air energy storage
Input(s)/Output(s) | n/m
Bases | Transformer
Balance | Mixed Integer Linear
Parameterization (not complete) | electrical_input, fuel input, electrical_output,
Examples | -
Note!
Set of equations can be found in Kaldemeyer, C.; Boysen, C.; Tuschy, I.
A Generic Formulation of Compressed Air Energy Storage as Mixed Integer Linear Program – Unit Commitment of Specific Technical Concepts in Arbitrary Market Environments Materials Today: Proceedings 00 (2018)
experimental

## Slide 20: Components- Current Developments
oemof-tabular.facades
provide energy specific access, provide an interface to tabular data sources from that models can be created easily. Map facade to energy systems.
Link: https://github.com/oemof/oemof-tabular/
Project: oemof_heat
Heat components for oemof e.g. heat pump, solar thermal collector, hot water storage, concentrating solar
Link: https://reiner-lemoine-institut.de/en/oemof_heat/
https://github.com/oemof-heat
(planned) Project: oemof_mobility

## Slide 21: Discussion
Questions?
Comments?

## Slide 22
Tel: +49 (0)30 1208 434 0
E-Mail: sarah.berendes@rl-institut.de
Web: http://www.rl-institut.de
Twitter: @rl_institut
License
Except where otherwise noted, this work and its content (texts and illustrations) are licensed under the Attribution 4.0 International (CC BY 4.0)
See license text for further information.
THANK YOU FOR YOUR ATTENTION !
How to follow Oemof’s activities?
Website: https://oemof.org/
Github: https://github.com/oemof
Or join our mailing list!
Please quote as: “oemof Component Models” © Reiner Lemoine Institut | CC BY 4.0